## Slide 1: 40 years of innovation in green sample preparation at RIC
Tatiana Cucu, Christophe Devos, Koen Sandra & Pat Sandra
2nd Green Analytical Chemistry Workshop
2nd of February 2026

## Slide 2
Privately owned European R&D partner in the field of analytical solutions mainly based on chromatography and electrophoresis in combination with mass spectrometry
Supporting customers worldwide in various industries with scientific know-how & technical expertise for 40 years
Founded by Prof. Pat Sandra in 1986
Now headed by Tom & Koen Sandra
Based in Belgium (Kortrijk)
French subsidiary (Lyon)
New state-of-the art facility since 2023
Introduction to RIC group

## Slide 3
Privately owned European R&D partner in the field of analytical solutions mainly based on chromatography and electrophoresis in combination with mass spectrometry
Supporting customers worldwide in various industries with scientific know-how & technical expertise for 40 years
Founded by Prof. Pat Sandra in 1986
Now headed by Tom & Koen Sandra
Based in Belgium (Kortrijk)
French subsidiary (Lyon)
New state-of-the art facility since 2023
Introduction to RIC group

## Slide 4
Our analytics
Sample preparation
Extraction/clean-up/preconcentration/
digestion/derivatization …
Small amounts of material
Separation
Detection
GC/LC/SFC/Electro-driven separations
MS(/MS), FID, UV, FLD, ELSD …
State-of-the-art equipment
Data/reporting
Data processing/reporting (quantification/ identification)
Statistical analysis

## Slide 5
“The best sample preparation is no sample preparation”
Today state-of-the-art instrumentation is very powerful, but sample preparation often remains the critical step in an analysis.
Success of sample preparation depends on:
  Extraction efficiency (matrix removal)
  Purification (isolation or selective extraction)
  Enrichment (through preconcentration of diluted samples)

## Slide 6
The 1999 Dioxin crisis in Belgium:
  Pat Sandra made the link between the dioxins and the PCBs (precursors)
  PCBs analysis in food – more simple, faster and cheaper
Green sample preparation at RIC
30 min extraction with 10 mL petroleum ether
5 mL extract + 1 g SiO2 containing 44% H2SO4 is added to remove the lipidic fraction
  Mixing for 30 min
Centrifugation and analysis
50 samples per day/instrument

## Slide 7
Green sample preparation at RIC
Solid Phase Microextraction (SPME) on a PDMS coated fused silica fiber:
  SPME followed by thermal desorption in a heated split/splitless injector (C.L. Arthur & J. Pawliszyn. Anal. Chem. 1990)
  Extraction of aqueous samples with a PDMS coated stir bar
    Baltussen E., Sandra P., David F., Cramers C (1999)

## Slide 8
Best sorptive extraction medium:
  PDMS is known to be one of the best stationary phases (apolar) in capillary GC
  Unique thermal stability and inertness: 50 – 400 °C
Why PDMS?
25 m x 0.25 mm ID x 0.25 µm df
10 m x 0.1 mm ID x 0.1 µm df
80 m x 0.1 mm ID x 0.1 µm df
Detailed PCBs analysis
Fast PCBs analysis

## Slide 9
Solventless extraction and analysis

## Slide 10
Recovery estimation
Predictable because PDMS/water distribution is similar to the octanol/water distribution
Ko/w can be used and if not available can be theoretically calculated
mSBSE= amount on PDMS
m0= initial amount
Kow = octanol - water partitioning
 = phase ratio
Thiobencarb – Log Ko/w : 3.8971 (Ko/w = 103.8971 = 7890)
SBSE
Twister: 24 µL PDMS
SPME
Fiber: 0.5 µL PDMS
Phase ratio β: 20 000
Phase ratio β: 416
Recovery: 95%
Recovery: 28%

## Slide 11
Green/solventless extraction technique
  Solventless = lower operational costs
Reduced staff exposure to hazardous solvents
Minimal sample manipulation and handling
  Can be used in the field for later analysis in an analytical lab
Can be re-used multiple times
Excellent repeatability and reproducibility
Sub ng/L sensitivity levels due to the higher volume of PDMS
Methods validated for many applications
SBSE advantages

## Slide 12
Excellent repeatability
Sesquiterpene fraction (common ion m/z 161)
EIC of m/z 88 characteristic for the ethyl esters
β-Santanol acetate
Beer 2
Beer 1

## Slide 13
Sampling in the field

## Slide 14
Sampling in the field?
  Analysis 1: immediately after sampling
  Analysis 2: after 3 days storage at 4°C
  Analysis 3: after 6 days storage at 4°C
β-Ocimene
Benzyl acetate
Benzenepropyl acetate

## Slide 15
SPME vs SBSE
SPME
SBSE

## Slide 16
Water analysis
Most official methods use liquid-liquid extraction with high solvent volumes or SPE:
  Dual SBSE extraction – single shot GC-MS/MS
  pg/L sensitivities
Water spiked at LOQs (n=6)

## Slide 17
Only PDMS ?
  Ongoing research in development of new phases (RIC group presentation Riva del Garda, Italy May 17-22, 2026)
Lack of extraction performance for polar compounds (log Ko/w < 2)
  Multiple/sequential SBSE extraction
  Salt addition
  Derivatization
  Addition of organic modifiers
  SA-SBSE
Limitations?

## Slide 18
Derivatization of perfluorocarboxylic acids by isobutyl chloroformate and SBSE extraction (Habib et al., 2024)
  Low ppt (ng/L) LOD obtained
  Excelent repeatability (below 15% at 100 ng/L)
Analysis of PFAS?

## Slide 19
How to achieve high analytical performance with limited environmental impact?
Sample throughput/productivity
  Cost per sample
(Ultra-) trace analysis
Multiresidues
  All in one run (e.g. pesticides in food and environmental samples, mineral oil, allergens in cosmetics, etc)
  Extractables and leachables
Challenges in sample preparation

## Slide 20
Time-consuming (cumbersome extraction procedures, lengthy concentration steps, etc)
High consumption of reagents and sample
Waste generation
High cost per analysis
Prone to human errors
Operator’s safety?
Conventional sample preparation techniques

## Slide 21
Reduce sample and solvent volume -> miniaturization
Minimize waste production
Use methods with higher extraction performance
Greener strategies in sample preparation

## Slide 22
Gerstel: comprehensive solutions for sample preparation

## Slide 23
Gerstel: comprehensive solutions for sample preparation

## Slide 24
Miniaturization
Reference method (ISO28540) PAHs in water | Miniaturized and automated
1 L of water + ISTD Target LOD = 1 ng/L | 15 mL water + ISTD Target LOD = 1 ng/L => 15 pg/15 mL sample
LLE with 25 mL hexane 100% recovery = 1 ng/25 mL hexane | µLLE with 3 mL hexane 100% recovery = 15 pg/3mL hexane
Recovery of the organic phase | Recovery of the organic phase (centrifugation?)
Drying on anh. Na2SO4 | Transfer of 1 mL to a 2 mL vial with anh. Na2SO4 100% recovery = 5 pg/1 mL
Concentration to 1 mL Final concentration: 1 ng/mL = 1 pg/µL | Vortex and centrifuge (optional) Final concentration: 5 pg/mL = fg/µL
GC-MS analysis 1 µL injection Amount on column: 1 pg | GC-MS/MS analysis 40 µL injection Amount on column: 0.2 pg
MS -> MS/MS
Reference method (ISO9377-2) Mineral oil in water | Miniaturized and automated
900 mL water + ISTD | 17 mL water + ISTD
LLE with 50 mL pentane | µLLE with 1 mL hexane
Shake (manually, one by one) | QuickMix (15 min)
Drying/Clean-up Na2SO4 & Florisil | Decap Transfer 600 µL to 2 mL vial with Na2SO4 & Florisil then Vortex
Concentration to 1 mL | -
GC-FID analysis 1 µL injection | GC-MS/MS analysis 100 µL injection (COC with EVE)
Notes: Add MCPD!

## Slide 25
Miniaturization & automation
Advantages of automation:
  Sustainable: enhanced precision, accuracy, and efficiency in laboratory processes
  Run 24/7 (unattended sample preparation or sample preparation & analysis)
  High throughput
    Combination with fast analysis
    Online and/or offline
  Low reagent consumption
  Extended application range (can be dedicated or can have several applications on a single workstation)
  Automation = more time for qualified staff for more important tasks

## Slide 26
Automated sample preparation options
Offline (preparation of vials for GC and LC analysis)
  Independent from the GC and LC run time
  Batch processing
  Safety (can be placed under fume hoods, separated ventilation)
Online (including injection in GC or LC)
  “fully automated”
  “just in time” sample preparation

## Slide 27
Preparation of the calibration solutions: VOC analysis in water
Preparation of the standard work solutions:
ISTD working solution preparation
STD working solution preparation
50 µL VOC 2
50 µL VOC 1
900 µL MeOH
Dilute 1/20
Dilute 1/10
Dilute 1/10
WS1
WS2
WS3
WIST 1
SIST 1

## Slide 28
Preparation of the calibration solutions & calibration curve
Addition of the STD/ISTD and analysis of samples and/or calibration
Working solution
preparation

## Slide 29
Calibration curves: VOC in water
10 – 5000 ppt
r2=0.999
Dichlorofluoromethane
Styrene
10 – 5000 ppt
r2=0.999

## Slide 30
Organic acids in urine/metabolomics studies (Fiehn method)
  Add ISTD and evaporate to dryness
  Add MOX and incubate at 40°C
  Add MSTFA/TMCS and incubate at 40°C
  Inject
Derivatization
“Just in time” analysis

## Slide 31
FAMEs analysis
Fatty Acids Methyl Esters:
  Food
  Biological samples
Online/Offline sample preparation and GC-FID analysis:
  ISO 16958: Using sodium methoxide (NaCH3O)
  ISO 12966-2: Using KOH/MeOH transesterification
  ISO 12966-4: Using BF3/MeOH

## Slide 32
FAMEs sample preparation
50 mg fat placed in a 20 mL vial (manual work)
Add MTBE containing ISTD
Vortex
Add NaCH3O
Vortex and wait
Add hexane (exactly 180s after the start of the reaction)
Add saturated NaCl solution
Vortex & centrifuge
Transfer hexane to a 2 mL vial with anh CaCl2
Vortex then inject
% FAME | Certificate | BF3 | KOH | NaOCH3
C16:0 | 10.74 | 10.80 | 10.93 | 11.01
C18:0 | 2.82 | 2.78 | 2.78 | 2.81
C18:1c | 25.40 | 24.91 | 25.08 | 24.97
C18:2c | 54.13 | 54.73 | 54.45 | 54.48
C18:3 n3 | 3.35 | 3.21 | 3.20 | 3.18

## Slide 33
Work in batch for increased sample throughput
Offline FAMEs analyzer
70 samples/24 h
Add 2 mL methylation reagent
Add 1 mL heptane
Incubate 1h in the agitator
Transfer for injection
Batch 12 samples
(2 agitators)
144 samples/24 h

## Slide 34
FAMEs in life science
Phospholipids FA analysis:
Compound name | Average rel. area | RSD
C16:0 | 0.22 | 2.60
C18:0 | 0.34 | 4.05
C18:1 | 0.70 | 2.40
C18:2 | 0.37 | 1.05
C20:3, n6 | 3.91 | 5.32
C20:3, n3 | 1.90 | 2.42
2 separate workstations
MPS Robotic Pro = 1 single configuration

## Slide 35
AOCS Cd 29a-13
  Acid catalysed transesterification (16h @ 40°C)
  Quantification of 2-, 3-MCPD and glycidol in one assay
AOCS Cd 29b-13
  Mild alkaline catalysed transesterification (16h @ -25°C)
  Quantification of 2-, 3-MCPD and glycidol in two assays
AOCS Cd 29c-13
  Fast alkaline catalysed transesterification
  Glycidol determined by difference (two assays)
Zwagerman-Overman method
  Fast alkaline transesterification at 10°C (exactly 12 min!)
  Quantification of 2-, 3-MCPD and glycidol in one single analysis
MCPD analysis in edible oils and fats
Preparation of calibration curves and sample analysis
  The only manual step: weigh 100 mg sample in a vial
Improved robustness:
  Addition of evaporation step to remove excess PBA reagent
  Injection via PTV (low temperature injection + LVI option)
  Pre-column backflushing for limited downtime due to column & source maintenance

## Slide 36
All in one?

## Slide 37
Solvent Assisted Flavor Extraction (SAFE) and GC-FID or GC-MS analysis
  Vacuum distillation -> cold trapping
  Time consuming, labor intensive, prone to formation of artifacts
  Use of toxic solvents (including dichloromethane, pentane, diethyl ether)
SPME analysis
  Lacks sensitivity and discrimination
Aroma analysis
Picture: https://research.reading.ac.uk/flavourcentre/flavour-analysis/flavour-extraction-techniques/

## Slide 38
Alternatives
Dynamic Headspace Sampling:
  Solventless extraction technique
  Continuous purging of headspace (sample) at controlled temperature for controlled time at controlled flow.
  Trapping of volatile organic compounds (adsorbent, sorbent, 20 °C – 70 °C)
  Thermal desorption of the compounds from the trap
  Goal: “exhaustive” extraction = highest sensitivity

## Slide 39
SAFE vs DHS: food aroma analysis
DHS
SAFE extract
Repeatability (n=5)

## Slide 40
SAFE vs SPME vs DHS: food aroma analysis

## Slide 41
VOC sampling from living plants: DHS large or active sampling

## Slide 42
DHS Large
Packaging material – 150°C

## Slide 43
Automated maintenance
Automated liner exchange (ALEX):
  QuEChERS extracts: insufficient cleaning
PTV injector with ALEX option:

## Slide 44
Automated maintenance
Automated liner exchange:
  Every 5 samples

## Slide 45
Conclusions
Take advantage of state-of-the-art GC and MS
Miniaturization <–> automation benefits:
  Reduced solvent consumption and waste production, increased productivity, safer
But…
  Sampling must be reconsidered in function of (automated) sample prep
  There is a minimum sample amount required for reliable analysis (sample homogeneity)
    Balance between miniaturization and experimental reliability is key
  New methods should be compared to existing ones and properly validated (certified materials, proficiency tests, demonstrate equivalence)
  Intuitive software interfaces for easy and user-friendly operation for users with varying levels of expertise (introduction in production sites)

## Slide 46
Complete turnkey solutions:
  From sampling, to sample preparation, to aquisition, to analysis, to reporting all automated
Simplification through further innovation (more sustainable in less time)
The future of sample preparation

## Slide 47
Organizing committee
Our colleagues at RIC group
Our partners & customers
Acknowledgements