## Slide 1
Unveil the MOSH &MOAH dimensionality by multidimensional chromatographic techniques
Giorgia Purcaro, Aleksandra Gorska, Paula Albendea
Gembloux Agro Bio-Tech, University of Liège, Belgium
gpurcaro@uliege.be

## Slide 2
Unveil the MOSH &MOAH dimensionality by multidimensional chromatographic techniques
Giorgia Purcaro, Aleksandra Gorska, Paula Albendea
Gembloux Agro Bio-Tech, University of Liège, Belgium
gpurcaro@uliege.be
A GAC perspective

## Slide 3
MOSH
Mineral oil saturated hydrocarbons
MOAH
Mineral oil aromatic hydrocarbons
MINERAL OIL HYDROCARBONS (MOH): DEFINITION*
n-alkane
isoalkane
cycloalkane
Aromatic hydrocarbons, mainly alkylated
a wide range of products deriving from petroleum distillation fractions

## Slide 4
MINERAL OIL HYDROCARBONS (MOH): OCCURENCE

## Slide 5
MOSH & MOAH: STATE-OF-THE ART
2012
2023
MOSH
MOAH
Generally considered of no concern at the concentration found.
genotoxicity of MOAH with ≥3 aromatic rings
in the absence of reliable toxicity data, the dietary exposure to 1–2 ring MOAH might raise a concern

## Slide 6
MINERAL OIL HYDROCARBONS (MOH)

## Slide 7
MOSH & MOAH: STATE-OF-THE ART
2012
2023
Generation of further data for the refinement of the risk assessment is needed
MOSH
MOAH
Generally considered of no concern at the concentration found.
genotoxicity of MOAH with ≥3 aromatic rings
in the absence of reliable toxicity data, the dietary exposure to 1–2 ring MOAH might raise a concern
Improvement of analytical methodology
for better characterisation of MOSH&MOAH and consistency in reporting

## Slide 8
Complex applications ↔ Advanced Routine
MOH
LC-GC-FID
MOSH & MOAH: Analytical Determination
Historical perspective
1989
1984
J Chromatogr. 1984 295:55-61
J High Resol Chromatogr. 1989 12:591–598.

## Slide 9
+ C11, C13 and CyCy (cyclohexylcyclohexane)
C11/CyCy loss of volatiles
C13/CyCy possible coelution
CyCy quantification
+ 5B (pentyl benzene), 1MN (1-Me Na) and 2MN (2-Me Na)
5B loss of volatiles
1MN=2MN possible coelution/ quantification
MOSH & MOAH: Analytical Determination
LC-GC-FID

## Slide 10
LC-GC-FID
LC
GC-FID
MOSH & MOAH: Analytical Determination
Sample dilution (e.g., fats and oil)

## Slide 11
Select direct analytical technique
Integrate analytical processes and operations​
Generate as little waste as possible​
Never waste energy​
Implement automation and miniaturization​
Favor reagents from renewable sources​
Increase safety for the operator​
Carry out in-situ measurements​
Avoid derivation​
Note minimal sample number and size​
Choose multi‑analyte or multi‑parameter methods​
Eliminate or replace toxic reagents​
GREEN CHEMISTRY
GREEN ANALYTICAL CHEMISTRY
S
I
G
N
I
F
I
C
A
N
C
E
UCM
Online method
Partially Automated
LC-GC-FID, no MS
Notes: 1. S Direct analytical techniques should be applied to avoid
sample treatment.
2. N Minimal sample size and minimal number of samples are
goals.
3. C In situ measurements should be performed.
4. I Integration of analytical processes and operations saves
energy and reduces the use of reagents.
5. I Automated and miniaturized methods should be selected.
6. A Derivatization should be avoided.
7. G Generation of a large volume of analytical waste should be
avoided and proper management of analytical waste should
be provided.
8. C Multi-analyte or multi-parameter methods are preferred
versus methods using one analyte at a time.
9. N The use of energy should be minimized.
10. F Reagents obtained from renewable source should be preferred.
11. E Toxic reagents should be eliminated or replaced.

## Slide 12
LC-GC-FID
LC
GC-FID
MOSH & MOAH: Analytical Determination
Sample dilution (e.g., fats and oil)
@Agree
Anal. Chem. 2020, 92, 10076−10082
Working range starting from 10 mg/kg
Max LC loading : 20 mg of fat
SENSITIVITY

## Slide 13
LC-GC-FID
LC
GC-FID
MOSH & MOAH: Analytical Determination
EXTRACTION/ENRICHMENT
Extraction and enrichment simultaneous
higher sensitivity, less frequent washing of the LC column.
Higher extraction yield

## Slide 14
LC-GC-FID
LC
GC-FID
MOSH & MOAH: Analytical Determination
EXTRACTION/ENRICHMENT
Extraction and enrichment simultaneous
higher sensitivity, less frequent washing of the LC column.
Higher extraction yield
Microwave-assisted saponification and extraction (MASE) method

## Slide 15
MOSH & MOAH: Analytical Determination
Microwave-assisted saponification and extraction (MASE) method
Moret S., Scolaro M., Barp L., Purcaro G., Conte, L.S., Food Chem 196 (2016) 50-57
MAS vs OVN-E (hexane)
5 × SENSITIVITY
More accurate information

## Slide 16
LC-GC-FID
MOSH & MOAH: Analytical Determination
Sample dilution (e.g., fats and oil)
@Agree
Anal. Chem. 2020, 92, 10076−10082
Working range starting from 10 mg/kg
Max LC loading : 20 mg of fat
LC-GC-FID
EXTRACTION/ENRICHMENT
Sensitivity (2 mg/kg*)
Accuracy
*Depends on the initial content of fat

## Slide 17
LC-GC-FID
MOSH & MOAH: Analytical Determination
Sample dilution (e.g., fats and oil)
@Agree
Anal. Chem. 2020, 92, 10076−10082
Working range starting from 10 mg/kg
Max LC loading : 20 mg of fat
Sensitivity (2 mg/kg*)
Accuracy
LC-GC-FID
EXTRACTION/ENRICHMENT
MASE applied for the meat:
5 g meat + 10 mL C6 + 10 mL KOH/(EtOH/H2O)
MASE: 5 min pre-heating, 120 °C 20 min
Albendea P., Purcaro G., Food Chemistry 480 (2025) 143880
Albendea P., Gorska A., Purcaro G., Journal of Chromatography Open 8 (2025) 100267
*Depends on the initial content of fat
MASE miniaturized:
0.4 g meat + 2.5 mL C6 + 2.5 mL KOH/(EtOH/H2O)
MASE: 5 min pre-heating, 120 °C 20 min
MINIATURIZATION
Warning on representativeness!

## Slide 18
MOSH & MOAH: Analytical Determination
@Agree
Anal. Chem. 2020, 92, 10076−10082
Sensitivity (2 mg/kg*)
Accuracy
LC-GC-FID
EXTRACTION/ENRICHMENT
*Depends on the initial content of fat
Microwave-assisted saponification and extraction (MASE) method

## Slide 19
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
LC
GC-FID
Microwave-assisted saponification and extraction (MASE) method
MOSH & MOAH: Analytical Determination
EPOXIDATION
Works rather well but also attacks MOAH due to their double bonds
ISO 20122:2024
Vegetable oils — Determination of mineral oil saturated hydrocarbons (MOSH) and mineral oil aromatic hydrocarbons (MOAH) with online-coupled high performance liquid chromatography-gas chromatography-flame ionization detection (HPLC-GC-FID) analysis — Method for low limit of quantification

## Slide 20
MOSH & MOAH: Analytical Determination
Need for matrix-tailored sample prep protocols
Data Interpretation
Data
Integration
> 20% of uncertainty!
Sample Preparation

## Slide 21
Select direct analytical technique
Integrate analytical processes and operations​
Generate as little waste as possible​
Never waste energy​
Implement automation and miniaturization​
Favor reagents from renewable sources​
Increase safety for the operator​
Carry out in-situ measurements​
Avoid derivation​
Note minimal sample number and size​
Choose multi‑analyte or multi‑parameter methods​
Eliminate or replace toxic reagents​
GREEN CHEMISTRY
GREEN ANALYTICAL CHEMISTRY
S
I
G
N
I
F
I
C
A
N
C
E
UCM
Online method
Partially Automated
LC-GC-FID, no MS
Notes: 1. S Direct analytical techniques should be applied to avoid
sample treatment.
2. N Minimal sample size and minimal number of samples are
goals.
3. C In situ measurements should be performed.
4. I Integration of analytical processes and operations saves
energy and reduces the use of reagents.
5. I Automated and miniaturized methods should be selected.
6. A Derivatization should be avoided.
7. G Generation of a large volume of analytical waste should be
avoided and proper management of analytical waste should
be provided.
8. C Multi-analyte or multi-parameter methods are preferred
versus methods using one analyte at a time.
9. N The use of energy should be minimized.
10. F Reagents obtained from renewable source should be preferred.
11. E Toxic reagents should be eliminated or replaced.

## Slide 22
LC-GC-FID
MOSH & MOAH: Analytical Determination
Sample dilution (e.g., fats and oil)
@Agree
Anal. Chem. 2020, 92, 10076−10082
Working range starting from 10 mg/kg
Max LC loading : 20 mg of fat
↑ Sensitivity (2 mg/kg*)
LC-GC-FID
EXTRACTION/ENRICHMENT
*Depends on the initial content of fat
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
Sample
Preparation
Data
Interpretation
Data
Integration
Uncertainty

## Slide 23
LC-GC-FID
MOSH & MOAH: Analytical Determination
Sample dilution (e.g., fats and oil)
@Agree
Anal. Chem. 2020, 92, 10076−10082
Working range starting from 10 mg/kg
Max LC loading : 20 mg of fat
↑ Sensitivity (2 mg/kg*)
LC-GC-FID
EXTRACTION/ENRICHMENT
*Depends on the initial content of fat
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
↑ Applicability
≈ Sensitivity
≈ ↑↓ Accuracy

## Slide 24
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
LC
GC-FID
Microwave-assisted saponification and extraction (MASE) method
MOSH & MOAH: Analytical Determination
The Source of Uncertainty
Sample
Preparation
Data
Interpretation
Data
Integration

## Slide 25
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
Ideal profile
MOSH & MOAH: Analytical Determination
without MOSH
NO MOAH
MOSH
~ 4 × MOAH
MOSH
MOAH
MOSH
MOAH
MOSH
MOAH
Same volatility range
Most probably not MOAH, but interferences
Data
Interpretation
Data
Integration

## Slide 26
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
Ideal profile
MOSH & MOAH: Analytical Determination
MOSH
MOAH
MOSH
MOAH
MOSH vs MOAH – No purification
Baseline
Riding peaks
Data
Interpretation
Data
Integration

## Slide 27
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
Ideal profile
MOSH & MOAH: Analytical Determination
MOSH
MOAH
Baseline
Riding peaks
Trimming or not the riding peaks? And how?
Data
Interpretation
Data
Integration

## Slide 28
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
Ideal profile
MOSH & MOAH: Analytical Determination
Trimming or not the riding peaks? And how?
Natural alkanes: primarily odd-chain in the ≥C21
Trim
MO alkanes: no prevalence
NO Trim
Baseline
Riding peaks
Data
Interpretation
Data
Integration

## Slide 29
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
Ideal profile
MOSH & MOAH: Analytical Determination
Trimming or not the riding peaks? And How?
Baseline
Riding peaks
Data
Interpretation
Data
Integration

## Slide 30
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
Ideal profile
MOSH & MOAH: Analytical Determination
GC×GC
How to support the interpretation?
N° of rings
Degree of alkylation
Data
Interpretation
Data
Integration

## Slide 31
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
Ideal profile
MOSH & MOAH: Analytical Determination
GC×GC
How to support the interpretation?
More accurate quantification

## Slide 32
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
Ideal profile
MOSH & MOAH: Analytical Determination
GC×GC
How to support the interpretation?
More accurate quantification
MOAH analysis by GC-FID
Iss coeluted with interferences
→ impossible MOAH quantification
MOAH
IS for quantification
MOAH analysis by GC×GC-FID

## Slide 33
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
Ideal profile
MOSH & MOAH: Analytical Determination
GC×GC
How to support the interpretation?
Easier interpretation
MOSH
MOAH

## Slide 34
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
Ideal profile
MOSH & MOAH: Analytical Determination
GC×GC
How to support the interpretation?
Easier interpretation
MOAH
MOAH

## Slide 35
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
Ideal profile
MOSH & MOAH: Analytical Determination
GC×GC
How to support the interpretation?
MOSH & MOAH
& sub-classes quantification in 2D
Bauwens, G., Panto, S., & Purcaro, G. (2021). Mineral oil saturated and aromatic hydrocarbons quantification: Mono- and two-dimensional approaches. Journal of Chromatography. A, 1643, 462044.doi:10.1016/j.chroma.2021.462044

## Slide 36
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
Ideal profile
MOSH & MOAH: Analytical Determination
GC×GC
How to support the interpretation?
G. Bauwens, L. Barp, G. Purcaro, Validation of the liquid chromatography-comprehensive multidimensional gas chromatography-time-of-flight mass spectrometer/flame ionization detector platform for mineral oil analysis exploiting interlaboratory comparison data, GreenAC (2023) 4 100047

## Slide 37
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
Ideal profile
MOSH & MOAH: Analytical Determination
GC×GC
How to support the interpretation?
G. Bauwens, L. Barp, G. Purcaro, Validation of the liquid chromatography-comprehensive multidimensional gas chromatography-time-of-flight mass spectrometer/flame ionization detector platform for mineral oil analysis exploiting interlaboratory comparison data, GreenAC (2023) 4 100047
Chart: MOSH
| IF-01 | IF-02 | IF-03 | IF-04 | IF-05 | IF-06 | IF-07 | IF-08 | IF-09 | IF-10 | IF-11 | IF-12 | IF-13 | IF-14 | IF-15
1D ILC | 5.8979 | 6.4074 | 4.9704 | 7.2413 | 8.1315 | 9.3704 | 11.4783 | 8.3242 | 10.5235 | 12.7042 | 18.7362 | 6.8318 | 9.198 | 18.4347 | 10.617
2D | 5.3 | 6.1182 | 5.275 | 6.8064 | 8.5325 | 9.8448 | 11.7924 | 9.1411 | 10.9876 | 13.3842 | 18.0695 | 6.86 | 8.5814 | 17.855 | 9.6021
Chart: MOAH – 2-MN
| IF-01* | IF-02 | IF-03 | IF-04 | IF-05 | IF-06 | IF-07 | IF-08 | IF-09 | IF-10 | IF-11 | IF-12 | IF-13 | IF-14 | IF-15
1D ILC | 0.43798 | 0.55279 | 0.36984 | 0.91746 | 1.256 | 1.806 | 2.4906 | 1.3804 | 2.1535 | 2.883 | 5.3338 | 1.0965 | 1.8228 | 5.1506 | 3.9896
2D | 0.58 | 0.50069 | 0.40147 | 0.82811 | 1.415 | 1.9033 | 2.741 | 1.5487 | 2.1607 | 2.8661 | 5.1554 | 1.1358 | 1.8632 | 4.5678 | 4.1158

## Slide 38
LC-GC-FID
MOSH & MOAH: Analytical Determination
Sample dilution (e.g., fats and oil)
@Agree
Anal. Chem. 2020, 92, 10076−10082
Working range starting from 10 mg/kg
Max LC loading : 20 mg of fat
↑ Sensitivity (2 mg/kg*)
LC-GC-FID
EXTRACTION/ENRICHMENT
*Depends on the initial content of fat
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
≈ Sensitivity
≈ ↑↓ Accuracy
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC×GC-FID
↑ Sensitivity
↑ Accuracy
↑ information

## Slide 39
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
Ideal profile
MOSH & MOAH: Analytical Determination
GC×GC
How to support the interpretation?
IMPROVEMENT ON SAMPLE PREP IS STILL NEEDED!
Sample
Preparation

## Slide 40
MOSH & MOAH: Analytical Determination
@Agree
Anal. Chem. 2020, 92, 10076−10082
ISO 20122:2024
Infant Formula
peak ratio between TBB and 2MN = 1.00
JRC Edible oil PT
Olive oil sample
Not specifically discussed, but discrepancies TBB/2MN observed from multiple labs
peak ratio between TBB and 2MN ≤1.25
total MOAH referred to TBB was constantly 13 % lower than the one obtained using 2MN.
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
Sample
Preparation

## Slide 41
MOSH & MOAH: New Advancements
Chart: New procedure (Bauwens & Purcaro, 2024)
| H2O (mL) | EtOH (mL) | Hexane (mL)
Percentage | 25 | 5 | 10
Chart: ISO 20122:2024
| H2O (mL) | EtOH (mL) | Hexane (mL)
Percentage | 5.5 | 7.5 | 10
Improved !!!
Reduction of the « polarity-based discrimination »
No matter the selected standard, the MOAH concentration would be the same
TBB/MN= 1.05±0.02
TBB/2MN: 1.19 ± 0.09
60°C × 30 min
60°C × 30 min
TBB/2MN: 1.05 ± 0.02
Chart: TBB/2MN ratio
| SFO | CCNO | RSO | palm | EVOO
Sap 1 wash 1 | 1.1324 | 1.1096 | 1.184 | 1.1702 | 1.0997
Sap 2 wash 3 | 1.0392 | 1.055 | 1.0483 | 1.062 | 1.0361
targeted value | 1 | 1 | 1 | 1 | 1
JRC tolerance | 1.15 | 1.15 | 1.15 | 1.15 | 1.15
DGF-ISO-20122 tolerance | 1.25 | 1.25 | 1.25 | 1.25 | 1.25
ISO 20122:2024
Bauwens&Purcaro
Matrix
Sample
Preparation
Bauwens, G., Purcaro, G., 2024. Improved microwave-assisted saponification to reduce the variability of MOAH determination in edible oils, Analytical Chimica Acta, 1312 342788

## Slide 42
MOSH & MOAH: New Advancements
Chart: New procedure (Bauwens & Purcaro, 2024)
| H2O (mL) | EtOH (mL) | Hexane (mL)
Percentage | 25 | 5 | 10
Chart: ISO 20122:2024
| H2O (mL) | EtOH (mL) | Hexane (mL)
Percentage | 5.5 | 7.5 | 10
Improved !!!
Reduction of the « polarity-based discrimination »
No matter the selected standard, the MOAH concentration would be the same
TBB/2MN: 1.19 ± 0.09
60°C × 30 min
60°C × 30 min
TBB/2MN: 1.05 ± 0.02
Chart: Residue (%)
| Fully hydrogenated rapeseed oil | Hydrogenated palm kernel olein | Rice bran oil
60°C - 30 min ISO | 0.52351 | 0.024399 | 0.030139
60°C - 30 min | 0.38695 | 0.11035 | 0.10971
90°C - 30 min | 0.012206 | 0.012675 | 0.057803
120°C - 30 min | 0.0080854 | 0.032573 | 0.027288
120°C - 20 min | 0.0034171
The method however showed to not be efficient on some high-melting matrices. So, time and temperature were re-optimized
Sample
Preparation
120 °C × 20 min
 | MASE TBB/2MN
Crude palm oil | 0.97 ± 0.01
No matrix | 1.02 ± 0.02
FH Palm Oil | 1.02 ± 0.05
FH Coconut Oil | 1.04 ± 0.02
Rice Bran Oil | 1.05 ± 0.05
Rapeseed Oil | 1.06 ± 0.01
FH Palm Kernel Olein | 1.07 ± 0.02
Coconut Oil | 1.07 ± 0.01
Fish Oil | 1.07 ± 0.02
Refined Palm Oil | 1.07 ± 0.05
Extra virgin olive oil | 1.13 ± 0.01
FH Rapeseed oil | 1.16 ± 0.00
TBB/MN= 1.05±0.01
Gorska, A., Ferrara, D., Albendea, P., Cordero, C. E., Purcaro, G., Update on the microwave-assisted saponification conditions for mineral oil hydrocarbons determination in fats and oils, Analyst, 2025,150, 5190-5200

## Slide 43
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
LC
GC-FID
MOSH & MOAH: Analytical Determination
EPOXIDATION
Works rather well but also attacks MOAH due to their double bonds
LC
GC-FID
Microwave-assisted saponification and extraction (MASE) method
Loss of 20-40% of MOAH
Sample
Preparation

## Slide 44
 | PALM OIL |  | SUNFLOWER OIL | 
 | /2MN | /PYR | /2MN | /PYR
MCPBA (nPO=2, nSFO=1) | *65% (± 21%) | *38% (± 7%) | 98% | 56%
PER AC C6 (n=3) | 177% (± 36%) | 105% (± 36%) | 146 (± 12%) | 124 (± 58%)
PER AC CHCl3 (n=3) | 79% (± 29%) | 61% (± 29%) | 61% (± 19%) | 47% (± 19%)
Purification
Oils spiked with 15 mg/kg (*7.5 mg/kg) of a mixture of of Gravex (very volatile MOAH), SN100 Aromatic Extract (mid volatility), SN500 Aromatic Extract (heavy fraction)
Low and Variable Recoveries!!!
MOAH RECOVERY (%)
Epoxidation performed manually
ROUTINE PURIFICATION METHOD
Sample
Preparation

## Slide 45
ISO 20122:2024 Vegetable oils — Determination of mineral oil saturated hydrocarbons (MOSH) and aromatic hydrocarbons (MOAH) with online coupled HPLC-GC-FID analysis — Method for low limit of quantification
Saponification + L/L extraction (C6)
SPE cleaning (only if needed)
Epoxidation (only if needed)
HPLC-GC-FID analysis
The issue with the current purification method for MOAH (i.e., epoxidation) is that it relies on a non-selective chemical reaction which also attacks MOAH.
It would therefore be relevant to develop a purification method which is not based on a chemical reaction anymore.
MOSH & MOAH: New Advancements
Sample
Preparation
Notes: POH Polyoligomeric hydrocarbons

## Slide 46
ISO 20122:2024 Vegetable oils — Determination of mineral oil saturated hydrocarbons (MOSH) and aromatic hydrocarbons (MOAH) with online coupled HPLC-GC-FID analysis — Method for low limit of quantification
Saponification + L/L extraction (C6)
SPE cleaning (only if needed)
Epoxidation (only if needed)
HPLC-GC-FID analysis
MOSH & MOAH: New Advancements
Saponification + L/L extraction (C6)
HPLC purification
HPLC-GC×GC-FID analysis
Sample
Preparation
Notes: POH Polyoligomeric hydrocarbons

## Slide 47
MOSH & MOAH: New Advancements
Saponification + L/L extraction (C6)
HPLC purification
HPLC-GC×GC-FID analysis
GC(×GC)
HPLC
C6/DCM gradient 1
MOSH
MOAH
Allure Silica (250 mm × 2.1 mm i.d. × 5 μm dp, 60 Å (Restek)
Gradient 1: 0 min 100% C6; 1.5–6 min 65% C6 35% DCM at 0.3 mL/min
Non-purified oil extract
(after saponification)
Sample
Preparation
Notes: POH Polyoligomeric hydrocarbons

## Slide 48
MOSH & MOAH: New Advancements
Saponification + L/L extraction (C6)
HPLC purification
HPLC-GC×GC-FID analysis
GC(×GC)
HPLC
MOSH
MOAH
Allure Silica (250 mm × 2.1 mm i.d. × 5 μm dp, 60 Å (Restek)
C6/DCM gradient 1
C6/DCM gradient 2
Gradient 1: 0 min 100% C6; 1.5–6 min 65% C6 35% DCM at 0.3 mL/min
Gradient 2: 0 min 100% C6; 1.5–14.5 min 98% C6 2% DCM; 14.5–23 min 95% C6 5% DCM at 0.3 mL/min
Sample
Preparation
Notes: POH Polyoligomeric hydrocarbons

## Slide 49
MOSH & MOAH: New Advancements
Saponification + L/L extraction (C6)
HPLC purification
HPLC-GC×GC-FID analysis
GC(×GC)
HPLC
Allure Silica (250 mm × 2.1 mm i.d. × 5 μm dp, 60 Å (Restek)
C6/DCM gradient 1
C6/DCM gradient 2
Gradient 1: 0 min 100% C6; 1.5–6 min 65% C6 35% DCM at 0.3 mL/min
Gradient 2: 0 min 100% C6; 1.5–14.5 min 98% C6 2% DCM; 14.5–23 min 95% C6 5% DCM at 0.3 mL/min
Purified MOAH
Sample
Preparation
Notes: POH Polyoligomeric hydrocarbons

## Slide 50
Sample
Preparation
MOSH & MOAH: New Advancements
Saponification + L/L extraction (C6)
HPLC purification
HPLC-GC×GC-FID analysis
Very good removal of carotenoids and squalene
Other terpenoids are less well removed
Notes: POH Polyoligomeric hydrocarbons

## Slide 51
MOSH & MOAH: New Advancements
Saponification + L/L extraction (C6)
HPLC purification
HPLC-GC×GC-FID analysis
Very good removal of carotenoids and squalene
Other terpenoids are less well removed
Epoxidation
mCPBA performic acid
82%± 10% 71 ± 16%
MOAH Recovery LC Purification:
94% ± 2%
Notes: POH Polyoligomeric hydrocarbons

## Slide 52
MOSH & MOAH: New Advancements
Saponification + L/L extraction (C6)
HPLC purification
HPLC-GC×GC-FID analysis
The LC purification method also allows to separate and quantify MOAH based on their number of aromatic rings.
Sample
Preparation
Notes: POH Polyoligomeric hydrocarbons

## Slide 53
Select direct analytical technique
Integrate analytical processes and operations​
Generate as little waste as possible​
Never waste energy​
Implement automation and miniaturization​
Favor reagents from renewable sources​
Increase safety for the operator​
Carry out in-situ measurements​
Avoid derivation​
Note minimal sample number and size​
Choose multi‑analyte or multi‑parameter methods​
Eliminate or replace toxic reagents​
GREEN CHEMISTRY
GREEN ANALYTICAL CHEMISTRY
S
I
G
N
I
F
I
C
A
N
C
E
UCM
Online method
Partially Automated
LC-GC-FID, no MS
Notes: 1. S Direct analytical techniques should be applied to avoid
sample treatment.
2. N Minimal sample size and minimal number of samples are
goals.
3. C In situ measurements should be performed.
4. I Integration of analytical processes and operations saves
energy and reduces the use of reagents.
5. I Automated and miniaturized methods should be selected.
6. A Derivatization should be avoided.
7. G Generation of a large volume of analytical waste should be
avoided and proper management of analytical waste should
be provided.
8. C Multi-analyte or multi-parameter methods are preferred
versus methods using one analyte at a time.
9. N The use of energy should be minimized.
10. F Reagents obtained from renewable source should be preferred.
11. E Toxic reagents should be eliminated or replaced.

## Slide 54
LC-GC-FID
MOSH & MOAH: Analytical Determination
Sample dilution (e.g., fats and oil)
@Agree
Anal. Chem. 2020, 92, 10076−10082
Working range starting from 10 mg/kg
Max LC loading : 20 mg of fat
↑ Sensitivity (2 mg/kg*)
LC-GC-FID
EXTRACTION/ENRICHMENT
*Depends on the initial content of fat
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC-FID
≈ Sensitivity
≈ ↑↓ Accuracy
EXTRACTION/SAPONIFICATION
PURIFICATION
LC-GC×GC-FID
↑ Sensitivity
↑ Accuracy
↑ information
EXTRACTION/SAPONIFICATION
LC-PURIFICATION
LC-GC×GC-FID
↑ Sensitivity
↑ ↑ Accuracy
↑ information

## Slide 55
CONCLUSION
MOSH & MOAH: How green are we?
Analytical evolution
Sensitivity ; Accuracy ; information

## Slide 56
https://www.extech2026.uliege.be/cms/c_20456371/en/extech-2026
JOIN
6-9 JULY 2026
GEMBLOUX AGRO-BIO TECH
BECAUSE SCIENCE IS THE KEY
https://www.extech2026.uliege.be

## Slide 57
Research team
Giorgia Purcaro
Sophie Vancraenenbroeck
Aleksandra Gorska
Damien Pierret
Damien Eggermont
Carlo Bellinghieri
Donatella Ferrara
Nicola Ruin
Thank you for the attention